Exercise 05: Feedback Analysis and simulation
<Advanced Analogue Building Blocks>
Kirchhoff-Institute for Physics, Uni-Heidelberg
Zhenxiong Yuan
2017.06.10

---
Contents
- A short review of feedback loop-gain
- Return ratio analysis for feedback loop
- Exercise:
  - Analysis of a capacitive-feedback amplifier
  - “stb” simulation in virtuoso

---
Overview of feedback
- Basic diagram of negative feedback
  - Loop-gain (T), closed-loop gain (A), …
  - Stability: phase margin, gain margin,...
- it’s not straight-forward to get the feedback diagram
  - Load effect from the feedback loop
  - Forward feedback by the feedback loop, …
- How to analysis a feedback loop?
  - Two-port network analysis
  - Return ratio methods
- Simulation: “stb” in Spectre

---
Return ratio
- Procedure for analysis loop-gain using return-ratio method
  - Set all independent sources to zero
  - Disconnect the dependent source from the rest of the circuit, which introduces a break in the feedback loop
  - On the side of the break that is not connected to the dependent source, connect an independent test source St of the same sign and type as the dependent source
  - Find the return signal Sr generated by the dependent source.
bold color maroon {T = -{{S_r} over {S_t} }}
[P. R. Gray, Analysis and design of analog integrated circuits, 5th edition]

---
Return ratio
- Analysis of closed-loop gain using return ratio method
- Very tedious to get this formula
  - Aoo: ideal closed-loop gain (idea amplifier, or set the coefficient of a dependent source to be infinity, and calculate the Vo/Vi )
  - d(s): gain of direct feed-through (set the coefficient of a dependent source to be zero, and calculate the Vo/Vi )
bold color maroon {A( s ) = A_{ infinity } { {T(s)} over {1+T(s)} } + {d(s)} over {1+T(s)} }

---
Exercise: analysis
- Capacitive-feedback amplifier with OTA used
  - Loop-gain
  - Closed-loop gain

---
Exercise: analysis loop-gain
- Derive Loop-gain expression T(s)
- Draw the bode-plot, calculate the bandwidth, unity gain-bandwidth
- Estimate the phase margin

---
Exercise: analysis closed-loop gain
- Calculate the full expression of d(s) and Aoo
- Simplify d(s) at frequency much higher than bandwidth of T(s)
- Simplify d(s) at low frequency and calculate the static gain-error

---
Exercise: simulation
In “Ex05/TB_OPA_stb”, using the stored states, do simulation. Try to understand the simulation result