Exercise 05: Feedback Analysis and simulation
<Advanced Analogue Building Blocks>
Kirchhoff-Institute for Physics, Uni-Heidelberg
Zhenxiong Yuan
2017.06.10

---
Contents
- A short review of feedback loop-gain
- Return ratio analysis for feedback loop
- Exercise:
  - Analysis of a capacitive-feedback amplifier
  - “stb” simulation in virtuoso

---
Overview of feedback
- Basic diagram of negative feedback
  - Loop-gain (T), closed-loop gain (A), …
  - Stability: phase margin, gain margin,...
- it’s not straight-forward to get the feedback diagram
  - Load effect from the feedback loop
  - Forward feedback by the feedback loop, …
- How to analysis a feedback loop?
  - Two-port network analysis
  - Return ratio methods
- Simulation: “stb” in Spectre

---
Return ratio
- Procedure for analysis loop-gain using return-ratio method
  - Set all independent sources to zero
  - Disconnect the dependent source from the rest of the circuit, which introduces a break in the feedback loop
  - On the side of the break that is not connected to the dependent source, connect an independent test source St of the same sign and type as the dependent source
  - Find the return signal Sr generated by the dependent source.
bold color maroon {T = -{{S_r} over {S_t} }}
[P. R. Gray, Analysis and design of analog integrated circuits, 5th edition]

---
Return ratio
- Analysis of closed-loop gain using return ratio method
- Very tedious to get this formula
  - Aoo: ideal closed-loop gain (idea amplifier, or set the coefficient of a dependent source to be infinity, and calculate the Vo/Vi )
  - d(s): gain of direct feed-through (set the coefficient of a dependent source to be zero, and calculate the Vo/Vi )
bold color maroon {A( s ) = A_{ infinity } { {T(s)} over {1+T(s)} } + {d(s)} over {1+T(s)} }

---
Exercise: analysis
- Capacitive-feedback amplifier with OTA used
  - Loop-gain
  - Closed-loop gain

---
Exercise: analysis loop-gain
- Derive Loop-gain expression T(s)
- Draw the bode-plot, calculate the bandwidth, unity gain-bandwidth
- Estimate the phase margin

---
Exercise: analysis loop-gain
v_x = {{C_f} over {C_f+C_s+C_x}} v_o = %beta v_o
%beta = {{C_f} over {C_f+C_s+C_x}}
Feedback ratio
v_o = -i_t( R_o {} parallel {} {1} over {sC_{L,tot}} )
Loading effect of feedback loop
C_{ L,tot } = C_L + ( 1-%beta )C_f
Effective loading
i_r = -i_t( R_o {} parallel {} {1} over {sC_{L,tot}} )G_m %beta
T( s ) = -{{i_r} over {i_t}} ={%beta G_m R_o} over {1+sR_o C_{L,tot}}
T_0 = %beta G_m R_o, { } %omega_p = {1} over {R_o C_{L,tot}},{ } %omega_c = T_0 %omega_p ,{ } PM approx 90

---
Exercise: analysis closed-loop gain
- Calculate the full expression of d(s) and Aoo
- Simplify d(s) at frequency much higher than bandwidth of T(s)
- Simplify d(s) at low frequency and calculate the static gain-error

---
Exercise: analysis closed-loop gain
Small signal circuit
Small signal circuit for calculating d(s)
A_{ infinity } = -{ {C_s} over {C_f} }
1. In the small signal circuit, set Gm to be infinity to calculate the Aoo
2. In the small signal circuit, set Gm to be 0 to calculate the d(s)
High frequency:
low frequency:
A_0 = - { {C_s} over {C_f} } { T_0 } over {1+ T_0 }
d approx {C_s C_f} over {C_f C_L + (C_x+C_s)(C_f+C_L)}
d approx 0
Static gain error:
A(s) = - { {C_s} over {C_f} } { {1 - {sC_f} over {G_m} } over {1+ {sC_{L,tot}} over {%beta G_m} } }
Zero in right half plan?
%varepsilon = {A_{infinity}-A_0} over {A_{infinity}} = {1} over {1+T_0} approx {1} over {T_0}
-3dB bandwidth?

---
Exercise: simulation
- The STB analysis linearizes the circuit about the DC operating poing and computes the loop-gain, gain and phase margins (if the sweep variable is frequency), for a feedback loop and a gain device.
- Refer to the Spectre Simulation Reference for details
- In “Ex05/OTA_LoopGain”, using the stored states, do simulation. Try to understand the simulation result
Try to understand the results if the simulation go beyond your expectation…
I am just too lazy to verify it when I prepare the exercise. Haha~