Exercise 06: Transient step response
<Advanced Analogue Building Blocks>
Kirchhoff-Institute for Physics, Uni-Heidelberg
Zhenxiong Yuan
2017.06.10

---
Contents
- Overview of transient step response
  - Linear setup for small step
  - Slew rate for large step
- Simulation and analysis: small step transient response
- Simulation and analysis: big step transient response

---
Linear setup
Consider a capacitive feedback circuit using single OTA
T( s ) ={%beta G_m R_o} over {1+sR_o C_{L,tot}}
A_o = - { {C_s} over {C_f} }, { } %omega_c = %beta {G_m} over {C_{L,tot}}
A(s) = - { {C_s} over {C_f} } { {1 - {sC_f} over {G_m} } over {1+ {sC_{L,tot}} over {%beta G_m} } } approx {A_o} over {1+ {s} over {%omega_c} } , { } C_{L,tot } >> %beta C_f
V_o( s ) = A( s ) cdot V_i( s ) = {{A_o} over {1+ {s} over {%omega_c} }} cdot { {V_{step}} over {s} }
v_o( t ) = - color green {{ {C_s} over {C_f} }V_{ step }} cdot color blue {{ {T_0} over {1+T_0} }} cdot color maroon {( 1 - func e^{-%omega_c t} )}
Static error
Dynamic error
color maroon {bold %tau = {1} / {%omega_c} }

---
simulation
- In “Ex6/OTA_Step”, using the parameters stored, do simulation and compare the results for different settings below:
  - Set Cs=Cf=500fF, CL=10pF, Vstep=10mV
  - Set Cs=Cf=500fF, CL=500fF, Vstep=10mV
- Analysis: what’s the effect of the zero on the dynamic settling time?

---
Slewing
- In “Ex6/OTA_Step”, using the parameters stored, do simulation and compare the results for different settings below:
  - Set Cs=Cf=500fF, CL=10pF, Vstep=1V
  - Calculate the slew rate, slewing time and settling time
- Analysis the slew rate, slewing time and settling time
  - For simple OTA
  - For two stage OTA